# United Nations Development Group Iraq Trust Fund

# Project: 55585 (E3 - 12-b)

# Date and Quarter Updated: 15th October 2008, 3rd Quarter – July to Sept 2008

| Participating UN Organisation: UN Office for Project Services (UNOPS) | Sector: Cluster E – Infrastructure Rehabilitation (WATSAN) |
| --- | --- |
| Govt of Iraq – Responsible Line Ministry : Ministry of Municipalities and Public Works (MMPW) |

# Programme/Project Number: E3 - 12-b

| Title | Rehabilitation of Takia Water Distribution System |
| --- | --- |
| Geographical Location | Takia sub-district town, Chamchamal District, Sulaymaniyah Governorate |
| Project Cost | US$ 2,006,340 |
| Duration | 9 months originally, extended up to 21 months |
| Approval Date (SC) | 27 February 2007 | Starting Date | April 2007 | Completion Date | December 2007-original Extended up to 31st Dec 08 |
| Project Description | Rehabilitation of the existing water distribution network, and the construction of reinforced concrete water storage tanks. |

# Development Goal and Immediate Objectives

The Development Goal of the project is to contribute towards improvement in the public health of the inhabitants by increasing the availability of safe drinking water. Immediate objectives: To significantly augment the quality and quantity of water supplied to 25,000 consumers in Takia by constructing a replacement reservoir and rehabilitating and extending the existing transmission mains utilising improved pipe materials and jointing techniques to reduce maintenance costs for the life of the new pipe system. To provide a comprehensive purpose-developed training in water supply network design and management to at least 30 technical staff of the Directorate of Water and Sanitation so as to improve quality and efficiency throughout the whole management cycle (planning, execution, monitoring) for service provision.

# Outputs, Key activities and Procurement

| Outputs | 25,000 consumers will have improved quantity and quality of water available brought about through reduced contamination and a reduction in losses in the pipe distribution system. Short-term employment creation for over 120 construction workers for a period of 9 months. Thirty (30) government employees are able to pass on their knowledge to others and to plan, implement, monitor and manage water supply projects in the urban areas demonstrated by improved on-the-job monitoring of operational sustainability issues to support service delivery and policymaking functions. |
| --- | --- |
| Activities | Survey, design and document the civil works and procure a contractor to install and/or rehabilitate the water mains and construct the reservoir Administer the civil works Contract; undertake quality control inspections; monitor project implementation; report project performance and provide security for personnel. Install and/or rehabilitate approximately 30 kilometres of water distribution network with extensions to the un-served areas of Takia town with the Construction of a 750 m3 reinforced concrete storage reservoir to reduce contamination in stored water. Hire and deploy an estimated 120 skilled and unskilled labourers from vulnerable groups, for the 9 month project duration; the workers being engaged, supervised and monitored by the civil works contractor to assist with construction of the network and reservoir. Deliver a purpose-designed training course of six-day duration to 30 technical personnel from the Ministry of Municipalities and Public Works, Directorate of Water and Sanitation on current design concepts for new or expanded networks; use of new materials and techniques to develop, rehabilitate, operate and maintain water distribution networks; the concept of ‘unaccounted for water’ and methods of reducing or eliminating such UFW; leakage detection and repairs. |
| Procurement (major items) and Onsite activities | The project has been awarded to M/s Dubai General Contracting Company for implementation of the project. Mobilization of material, man power and equipments has started. All High Density Polyethylene pipes (HDPE) 90mm and 20 mm where supplied on site in addition to the entire related PE fittings. 30% of main Ductile iron pipes were also supplied The locations of wells were identified with the aid of the Sulymania Water Directorate’s Geology unit and drilling of one well completed and other one is under progress. Construction of 750 cum tank was completed. Drilling of second bore well, construction of second pump house cum guard room and laying of pipelines are progressing as planned. |

# Situation as of 30/09/2008

| Funds Committed | US$1,755,378 | % of approved | 87.5 |
| --- | --- | --- | --- |
| Funds Disbursed | US$847,685 | % of approved | 42.25 |
| Forecast final date | December 2008 | Delay (months) | 12 months |

# Quantitative achievements against objectives and results

| Site preparations and contract awarding for civil work | Survey, design and document the civil works with full specifications was finalized. A contractor to install and rehabilitate the water mains and construct the reservoir was chosen and awarded. Mobilization of Material, manpower and equipment was fully completed. | % of planned | 100 |
| --- | --- | --- | --- |
| Procurement of pipes and fitting | All High Density Polyethylene pipes (HDPE) 90mm were supplied on site in addition to the entire related PE fittings. All pipes and fitting were strictly crosschecked against the ISO 9001 certification from the International Organization for Standardization and were approved | % of planned | 80 |
| Civil work and rehabilitation | Drilling of Deep Wells – One completed and the other one is progressing well. Pump house & Guard Room – One completed and the other one is progressing well. Concrete ground water tank of 750 cum – Completed. Laid 3.5 km of pipeline and laying of remaining length is ongoing. | % of planned | 75 |
| Training | The training programme has been conducted between 30th August to 6th September 2008. | % of planned | 100 |

# Qualitative achievements against objectives and results

Several technical meetings were conducted in Sulymania water directorate to set the plans for a smooth implementation process. The Procurement component of the project is progressing as scheduled. The layout plan to lay the pipeline was solved with the help of government officials in Takia. However, the supply of pipe materials as agreed during the project preparation is yet to be considered. This is delaying the project implementation with regards to the schedule. UNOPS staff is meeting regularly with all stakeholders to ensure efficient and successful coordination, monitoring and evaluation of the implementation of the project activities. The dispute over land ownership of Ground Level Reservoir (GLR) site was solved and construction water tank was completed. An unforeseen dispute over the possession of land which had been considered for the construction of the water tank affected the progress of the project. UNOPS representatives are urging the Governorate Officials to stick to their commitment of providing the pipe materials as soon as possible to complete the project in time.